Tradeoff Analysis

The following tradeoff analysis documents the various technologies considered for various system functions, broken down by component: the Personnel Locator (PL), the Signal Posts (SP), and the Command Center (CC).

Personnel Locator

Location Determination

- Cellular Base Station Triangulation

- Global Positioning System

- PATS-specific Radio Frequency based Tri-lateration with Signal Posts

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Terrestrial-based Infrastructure available in populated areas Standards are published and open Line of sight not required Hardware is readily available | No global standard, only regional Remote areas do not have coverage Need collaboration with base station owners May incur monetary costs |
| 2 | Available worldwide Maintained by the U.S. Air Force Passive device, no collaboration with equipment owners needed Free to receive GPS signals Hardware is readily available | Line of sight required |
| 3 | Mission-specific design RF design well understood by many contractors (i.e. Motorola, Texas Instruments, Kenwood, etc.) Line of sight not required | New implementation; design not ubiquitous |

Communications

- Infrared Optical

- Radio Frequency Single Frequency Band (Digital)

- Radio Frequency Single Frequency Band (Analog)

- Radio Frequency Multiple Frequency Band (Digital)

- Radio Frequency Multiple Frequency Band (Analog)

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | IrDA specifications/standards available Hardware is readily available | Line of sight required Susceptible to disturbances Distance is limited |
| 2 | Mission-specific design Digital communications preserves battery life RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 3 | Mission-specific design Analog communications requires more power RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 4 | Mission-specific design Digital communications preserves battery life Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |
| 5 | Mission-specific design Analog communications requires more power Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |

  - Ultra Low Frequency

  - Very High Frequency

Table 1:  RF Technologies Trade

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Can penetrate water and earth Currently used in TTE communications for mine safety | Slow data rate Susceptible to electronic interference |
| 2 | Currently used in broadcast television Higher robustness to atmospheric and earth interference Higher data rates | Less able to penetrate earth and water |

Identification

- Internal Programmable Flash Memory

- Internal Read-Only Memory

- Removable Flash Memory

- Radio Frequency Identification (RFID)

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Simple design Can be programmed Internal to PL | Replacement requires disassembly Programming interface needs to be designed Cannot detect if “PL separated from wearer” |
| 2 | Simple design Internal to PL | Replacement requires disassembly Once programmed, contents not easily changed Cannot detect if “PL separated from wearer” |
| 3 | Simple design Many removable flash memory products exist Can be moved easily from one PL to another Can be written via card reader | Removable parts are easily lost Additional item to be carried Cannot detect if “PL separated from wearer” |
| 4 | Simple design Incorporated into employee ID badge RFID a well established technology Allows for detection of “PL separated from wearer” | Programming requires special equipment |

Distress Notification

- Autonomous

- Manual

- Hybrid (Autonomous and Manual)

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | No user interaction is necessary No input interface needed | Prone to false alarms |
| 2 | Less prone to false alarms | User interaction is necessary Input interface required |
| 3 | Allows user to manually issue a distress notification Allows user to manually disable a distress notification | User interaction may be required |

Display

- No Display Provided

- Light Emitting Diodes

- Liquid Crystal Display

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Simple enclosure design Easily ruggedized | No user insight into PL operational status |
| 2 | Simple enclosure design | Limited user insight into PL operational status |
| 3 | Provides maximum insight into PL operational status Allows user to manually disable a distress notification | Complex enclosure design Difficult to ruggedize |

Signal Posts

Location Determination

- Cellular Base Station Triangulation

- Global Positioning System

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Terrestrial-based Infrastructure available in populated areas Standards are published and open Line of sight not required Hardware is readily available | No global standard, only regional Remote areas do not have coverage Need collaboration with base station owners May incur monetary costs |
| 2 | Available worldwide Maintained by the U.S. Air Force Passive device, no collaboration with equipment owners needed Free to receive GPS signals Hardware is readily available | Line of sight required |

Communications

- Infrared Optical

- Radio Frequency Single Frequency Band (Digital)

- Radio Frequency Single Frequency Band (Analog)

- Radio Frequency Multiple Frequency Band (Digital)

- Radio Frequency Multiple Frequency Band (Analog)

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | IrDA specifications/standards available Hardware is readily available | Line of sight required Susceptible to disturbances Distance is limited |
| 2 | Mission-specific design Digital communications preserves battery life RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 3 | Mission-specific design Analog communications requires more power RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 4 | Mission-specific design Digital communications preserves battery life Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |
| 5 | Mission-specific design Analog communications requires more power Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |

Table 2:  RF Technologies Trade1

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Can penetrate water and earth Currently used in TTE communications for mine safety | Slow data rate Susceptible to electronic interference |
| 2 | Currently used in broadcast television Higher robustness to atmospheric and earth interference Higher data rates | Less able to penetrate earth and water |

Command Center

Communications

- Infrared Optical

- Radio Frequency Single Frequency Band (Digital)

- Radio Frequency Single Frequency Band (Analog)

- Radio Frequency Multiple Frequency Band (Digital)

- Radio Frequency Multiple Frequency Band (Analog)

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | IrDA specifications/standards available Hardware is readily available | Line of sight required Susceptible to disturbances Distance is limited |
| 2 | Mission-specific design Digital communications preserves battery life RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 3 | Mission-specific design Analog communications requires more power RF design well understood by many contractors | New implementation; design not ubiquitous Single RF frequency band limits flexibility and performance |
| 4 | Mission-specific design Digital communications preserves battery life Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |
| 5 | Mission-specific design Analog communications requires more power Multi-band RF provides flexibility RF design well understood by many contractors | New implementation; design not ubiquitous |

Computer Hardware

- PATS-specific Proprietary Designed Computer

- Standard x86-based Computer

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Mission-specific design | Special training maybe required Uncertain upgrade path Design may me lengthy May require a new operating system Expensive |
| 2 | Standardized equipment Readily available operating system choices New hardware continually released Cost effective: no new design needed | Hardware selected during the requirements phase maybe obsolete by the implementation phase |

Operating System

- Linux

- Macintosh OS

- Microsoft Windows

| Option | Strengths | Weaknesses |
| --- | --- | --- |
| 1 | Open source Large developer base Runs on standard x86 hardware architecture | Can lack polish Community based support structure |
| 2 | Polished and consistent user interface | Closed source Limited developer base Requires Apple hardware |
| 3 | Polished and consistent user interface Large developer base User support backed by a large corporation Runs on standard x86 hardware architecture | Closed source |

# Footnotes

"Radio frequency." Wikipedia, The Free Encyclopedia. 19 Oct 2009, 08:17 UTC. 19 Oct 2009 <http://en.wikipedia.org/w/index.php?title=Radio_frequency&oldid=320760634>.