VTOL Research

V22 Osprey	1

F-35 Lighning II	4

Apache	6

Black Hawk	8

S-76 Medivac	11

MD500	14

MD500 Defender	17

UAV Capable	19

Camcopter S-100	19

Fire Scout MQ8	20

A-160 Hummingbird (YMQ-18A)	22

Eagle Eye	24

Flying-Cam	26

Organic Air Vehicle	30

Small Unmanned Air Vehicle	30

RQ-16 T-Hawk	32

Vigilante	35

Baldwin MonoTiltRotor	35

# V22 Osprey

# F-35 Lighning II

# Apache

http://www.howstuffworks.com/apache-helicopter.htm

http://en.wikipedia.org/wiki/AH-64_Apache

| Specifications |
| --- |
| Contractors | Boeing McDonnell Douglas Helicopter Systems (Mesa, AZ) General Electric (Lynn, MA) Martin Marietta (Orlando, FL) |
| Variant | AH-64A | AH-64D |
| Propulsion | Two T700-GE-701Cs |
| Length | 58.17 ft (17.73 m) | 58.17 ft (17.73 m) |
| Height | 15.24 ft (4.64 m) | 13.30 ft (4.05 m) |
| Wing Span | 17.15 ft (5.227 m) | 17.15 ft (5.227 m) |
| Primary Mission Gross Weight | 15,075 lb (6838 kg) 11,800 pounds Empty | 16,027 lb (7270 kg) Lot 1 Weight |
| Hover In-Ground Effect (MRP) | 15,895 ft (4845 m) [Standard Day] 14,845 ft (4525 m) [Hot Day ISA + 15C] | 14,650 ft (4465 m) [Standard Day] 13,350 ft (4068 m) [Hot Day ISA + 15 C] |
| Hover Out-of-Ground Effect (MRP) | 12,685 ft (3866 m) [Sea Level Standard Day] 11,215 ft (3418 m) [Hot Day 2000 ft 70 F (21 C)] | 10,520 ft (3206 m) [Standard Day] 9,050 ft (2759 m) [Hot Day ISA + 15 C] |
| Vertical Rate of Climb (MRP) | 2,175 fpm (663 mpm) [Sea Level Standard Day] 2,050 fpm (625 mpm) [Hot Day 2000 ft 70 F (21 C)] | 1,775 fpm (541 mpm) [Sea Level Standard Day] 1,595 fpm (486 mpm) [Hot Day 2000 ft 70 F (21 C)] |
| Maximum Rate of Climb (IRP) | 2,915 fpm (889 mpm) [Sea Level Standard Day] 2,890 fpm (881 mpm) [Hot Day 2000 ft 70 F (21 C)] | 2,635 fpm (803 mpm) [Sea Level Standard Day] 2,600 fpm (793 mpm) [Hot Day 2000 ft 70 F (21 C)] |
| Maximum Level Flight Speed | 150 kt (279 kph) [Sea Level Standard Day] 153 kt (284 kph) [Hot Day 2000 ft 70 F (21 C)] | 147 kt (273 kph) [Sea Level Standard Day] 149 kt (276 kph) [Hot Day 2000 ft 70 F (21 C)] |
| Cruise Speed (MCP) | 150 kt (279 kph) [Sea Level Standard Day] 153 kt (284 kph) [Hot Day 2000 ft 70 F (21 C)] | 147 kt (273 kph) [Sea Level Standard Day] 149 kt (276 kph) [Hot Day 2000 ft 70 F (21 C)] |
| Range | 400 km - internal fuel 1,900 km - internal and external fuel |  |

# Black Hawk

http://en.wikipedia.org/wiki/UH-60_Black_Hawk

http://science.howstuffworks.com/black-hawk.htm

# S-76 Medivac

http://en.wikipedia.org/wiki/Sikorsky_S-76

http://en.wikipedia.org/wiki/Traumahawk

http://en.wikipedia.org/wiki/CAMTS

# MD500

http://en.wikipedia.org/wiki/MD_Helicopters_MD_500

# MD500 Defender

http://en.wikipedia.org/wiki/MD_500_Defender

# UAV Capable

## Camcopter S-100

## Fire Scout MQ8

## A-160 Hummingbird (YMQ-18A)

http://www.globalsecurity.org/intell/systems/a160.htm

## A160 Hummingbird Warrior

On 04 May 2004 Boeing announced it had acquired Frontier Systems Inc., developer of the A-160 Hummingbird and Maverick unmanned aerial vehicles (UAV). Frontier’s platforms and technologies add to Boeing’s portfolio and capabilities in unmanned systems that include the Joint Unmanned Combat Air System X-45, ScanEagle and other concepts under development. Frontier also sells the Maverick UAV, a retrofitted commercially available helicopter, to the U.S. Special Operations Command. The Maverick UAV has also been used as a test bed for A-160 technologies.

The A-160 Hummingbird, a vertical take-off-and-landing UAV, has been designed to fly up to 2,500 plus nautical miles with 30 to 40 hour endurance. Its modular payload design can carry up to 1,000 pounds. The A-160 offers range and endurance unprecedented in the history of helicopter UAV design. It will provide reconnaissance, surveillance, target acquisition, communication relay, precision re-supply, sensor delivery and eventually precision attack capabilities.

The A160 Hummingbird, built by DARPA and Frontier Aviation of San Diego, will exploit a hingeless, rigid rotor concept operating at the optimum rotational speed to produce a vertical take-off and landing (VTOL) unmanned air vehicle (UAV) with very low disk loading and rotor tip speeds resulting in an efficient low power loiter and high endurance system. This unique concept offers the potential for significant increases in VTOL UAV range (more than 2,000 nm) and endurance (24-48 hours). Detailed design, fabrication and testing of this vehicle is being conducted to establish its performance, reliability, and maintainability. The A160 concept is being evaluated for surveillance and targeting, communications and data relay, lethal and non-lethal weapons delivery, assured crew recovery, resupply of forces in the field, and special operations missions in support of Army, Navy, Marine Corps, and other Agency needs. It is being developed as a component of the DARPA/Army Future Combat Systems (FCS) Program. In addition, this program will evaluate application of the optimum speed rotor concept to other systems including heavy lift and tilt rotor capabilities. The program will also develop highly efficient heavy fuel engine technologies to further advance current range and endurance projections as well as improve operational reliability and logistics compatibility.

The Army's Advanced Rotary Wing Vehicle (RWV) Technology project matures and demonstrates rotary wing unmanned and manned platform technologies for the Objective Force. It is envisioned that the Objective Force will need unmanned and manned rotorcraft systems that have significantly increased/improved lift, range and survivability with an overall reduction in logistics. Key to this effort is the demonstration of a vertical takeoff and landing (VTOL) UAVs for the Objective Force. The critical technologies to support these capabilities will be matured through Technology Demonstrations (TDs) of prototype UAVs, rotors, active controls, structures, drive train, and threat protection. The near term demonstration of unmanned, VTOL UAVs will focus on the A-160 Hummingbird UAV and the Organic Air Vehicle (OAV), to include the Micro Air Vehicle variant, for Reconnaissance, Surveillance and Target Acquisition (RSTA) capability. These demonstrations will focus on military operations and the application of military specification on these maturing systems.

The A-160 Hummingbird is a DARPA project to produce an unmanned helicopter that can fly 2,500 nautical miles over 40 hours and carry 300 pounds of air-to-ground missiles. The Army wants to take over the project in 2003 (years ahead of schedule) in order to ensure that the aircraft ends up being what the Army wants it to be. A production decision would be made around 2006. The A-160 has a 300hp internal combustion engine and a three-bladed rotor. The Army plans to add a tactical common data link in order to receive the aircraft's data and direct its flight and weapons.

The A160 helicopter demonstrator, about the size of the Predator-A, was built by Abraham Karem and his team at Frontier Systems of Irvine, California, under contract to DARPA. The A160's predicted top speed is 140 knots." The Hummingbird is 35 feet long with a 36-foot rotor diameter. The A160 prototype made its first forward flight on 29 January 2002.

The A160 will have range, endurance, and altitude capabilities unprecedented in the history of helicopter design. The A160 has a conventional main-tail-rotor helicopter configuration, but the conventional appearance is misleading. A contemporary helicopter features lightweight flexible rotors that are connected to the rotor hub through articulated joints. Such rotors are designed to provide smooth flight operation with little vibration and good control authority.

However, they can only do so within a limited range of speeds, normally at as high an RPM as possible before the wingtips break the sound barrier. The helicopter's rotor RPM is roughly constant while the aircraft is in flight. This is inefficient, particularly when the helicopter is flying below maximum speed or with an optimal load.

The A160's carbon-fiber composite rotor blades are tapered, and their cross-section varies from root to tip. They are light but stiff to avoid vibration, and their stiffness also varies from root to tip. The rotor system is rigid and hingeless, and features a larger diameter and lower disk loading than that of a conventional helicopter with the same lift capacity.

The A160 rotor can be operated from 140 to 350 RPM. Coupled with a fuel-efficient piston engine results in a helicopter that not only has unbelievable fuel efficiency, but good speed, unprecedented altitude capability, and is very silent.

The A160 project began in early 1998, with Frontier Systems modifying a light commercial Robinson R22 helicopter to a UAV configuration to test flight-control systems. The R22 was lost in an accident in early 2000, but not before it had flown for 215 hours under autonomous control. The innovative A160 rotor system is now being ground tested.

The A160 demonstrator will weigh about 1,800 kilograms (4,000 pounds), and will have rotor blades 5.2 meters (17 feet) long. The demonstrator will be powered by a commercial piston engine with over 300 horsepower, and will have a payload capacity of more than 135 kilograms (300 pounds). Possible payloads include EO/IR imaging and SAR sensors. Apparently there is work being done on integrating SAR receiving antennas into the rotors themselves, though the transmit antenna will be mounted on the fuselage.

The demonstrator, which was given the name "Hummingbird", will have a top speed of 260 KPH (160 MPH), 24 to 36 hours endurance, 5,500 kilometer (3,450 mile) range, and a flight ceiling of 9,150 meters (30,000 feet). A production version could have an endurance of up to 48 hours and a ceiling of 16,800 feet (55,000 feet). First flight was in early 2002.

The A160 is a technology development exercise and is not being designed for a specific operational mission, but its general design concept envisions a UAV that could deploy itself from the US to a combat area, or perform deep penetrations into hostile territory. The US Army and the US Special Operations Command (SOC) are interested in the project, with the SOC considering uses such as extracting troops trapped behind enemy lines.

## Eagle Eye

## Flying-Cam

## Organic Air Vehicle

The Organic Air Vehicle, or OAV, program will provide the individual soldier with the capability to detect the enemy concealed in forests or hills, around buildings in urban areas, or in places where the soldier does not have a direct line-of-sight. OAVs can perch and stare, and essentially be sentinels for maneuvering troops. Rather than sending a soldier into harm?s way to scout a particularly dangerous area, the unit can now use the OAV instead.

PLATFORM CHARACTERISTICS SET A

Soldier level asset

Soldier transportable
Gross Weight: 20 lbs
Endurance: 15 minutes
Range: 1 km
Payload: 1 lb
Ceiling: 8000 ft MSL
Low Acoustic Signature: 75 db @ 20 ft
VTOL or STOL (Vertical or Short Takeoff/Landing)
Diesel fuel engine
Payload type: EO/IR
Performance characteristics based on Army Standard Day (4000 ft, 95 F)
Performance values noted above are approximate.

PLATFORM CHARACTERISTICS SET B

Platoon level asset

Carrier transportable (Hummer size)
Gross Weight: 75 lb
Endurance: 25 minutes
Speed: Vmax > 40 kts
Range: 2 km
Payload: 7 lb
Ceiling: 8000 ft MSL
Low Acoustic Signature: 75 db @ 100 ft
Day/Night operations
VTOL (Vertical Takeoff/Landing)
Diesel fuel engine
Tethered options will be considered
Primary Payload Type: EO/IR
Alternate Modular Payloads: Acoustic, Mine Detection, Comm-Relay, SIGINT
Performance characteristics based on Army Standard Day (4000 ft, 95 F)
Performance values noted above are approximate.

## Small Unmanned Air Vehicle

Current Army research has shown that the next conflict will most likely be fought in complex terrain/urban environments where LOS will decide the survivability of the small unit/scout. The small unit/scout is limited in its reconnaissance & surveillance mission only by what it can or cannot see. An SUAV with VTOL/NLOS capability would increase the "sight" of the small unit/scout by going around a corner or between buildings where LOS is broken and giving a visual image to the operator in Near Real Time (NRT).

The Future Combat System (FCS) Unmanned Air Vehicle (UAV) plan consists of a family of several types of airborne vehicles, including the Small UAV (SUAV). This BIA requests proposals for the definition and refinement of the SUAV platform, definition of common subsystem interfaces, specification development, ROM costs models, and System Development and Demonstration (SDD) program plans.

Small Unmanned Air Vehicle - Desired Functional & Performance Characteristics

PLATFORM CHARACTERISTICS SET A

Tube Launched

Low cost tube launched (air or ground launch)
Mission: RSTA
Non-organic refurbishment
Sensor recovery
Gross Weight: 300 lbs
Endurance: 6 hr
Altitude: 500 - 1500 ft AGL
Speed: Vmax > 80 kts
Radius: 10 km
Payload: 75 lbs
Signature: Low IR, Low Acoustic
Day/Night operations
Parachute recovery
Diesel fuel engine
Primary Payload Type: EO/IR
Alternate Payloads: NBC Detection, Comm-Relay, Lethal
Performance characteristics based on Army Standard Day (4000 ft, 95 F)
Performance values noted above are approximate.

PLATFORM CHARACTERISTICS SET B

VTOL (Vertical Takeoff/Landing)

Low-cost RSTA
Ground Vehicle Based
Gross Weight: 150 lb
Endurance: 2 hrs
Speed: Vmax > 80 kts
Range: 8 km
Payload: 40 lbs
Signature: Low IR, Low Acoustic
Day/Night operations
VTOL
Diesel fuel engine
Primary Payload Type: EO/IR
Performance characteristics based on Army Standard Day (4000 ft, 95 F)
Performance values noted above are approximate

## X50 Dragonfly

http://en.wikipedia.org/wiki/Boeing_X-50

http://www.globalsecurity.org/military/systems/aircraft/x-50.htm

http://www.darpa.mil/body/NewsItems/ucav/A1604blade5t%20flight2-10-03.mpg

# X-50 Dragonfly Canard Rotor/Wing (CRW)

The Army, Navy and Marine Corps have a need for affordable, survivable, vertical take-off and landing (VTOL) air vehicles to support dispersed units in littoral and urban areas. The Canard Rotor/Wing (CRW) program explores innovative VTOL technologies and concepts with the potential for significant performance improvements that would satisfy stressing mission needs. One such concept is the advanced Canard Rotor/Wing (CRW) aircraft, that offers the potential for a high speed rapid response capability from a VTOL unmanned air vehicle with significant range and stealth improvements as compared to other VTOL concepts. Design and fabrication of this scaled vehicle concept will validate the command and control, stability and control system and aerodynamic performance required for vertical take-off, landing and hover via a rotating center wing that stops and locks in place for efficient high speed cruise.

An operational CRW UAV would be able to take off and land in confined areas without a launch or recovery system, rapidly transition to and from a fixed wing mode and fly at speeds in access of 375 knots. The flexibility achieved through these various flight modes, combined with the high-speed performance and survivability of this revolutionary new concept makes the CRW an exciting option for manned and unmanned applications.

Boeing has leveraged specific expertise that was developed during the company's previous work on reaction drive rotor systems, including both the XH-17 in the early 1950s and the XV-9A in the mid-1960s. The Boeing patented CRW concept is an outgrowth from these previous activities.

In response to a Navy requirement for an unmanned, high-speed, ship-based vertical take off and landing (VTOL), McDonnell Douglas Helicopter developed a concept called Canard-Rotor-Wing (CRW). The CRW is a stoppable-rotor design which can hover and fly at low-speeds like a conventional helicopter, whereas in its stopped-rotor mode it can fly at high speeds comparable to those of fixed-wing aircraft. Initial concepts include a land- or ship-based medium-range vertical takeoff and landing, remotely piloted vehicle. An operational CRW UAV would be able to take off and land in confined areas without a launch or recovery system, rapidly transition to and from a fixed wing mode and fly at speeds in access of 375 knots.

The CRW is propelled in both rotary-wing and fixed-wing modes using a conventional turbofan engine. A diverter valve directs the exhaust gas produced by the engine either to the rotor or aft to the jet thrust nozzle, or to both during transition. A two-bladed teetering rotor is used to generate the required lift for hover and low-speed forward flight. The CRW would spin a center wing to take off like a helicopter.The vehicle would then accelerate to about 120 knots when flaps would deploy from the front and rear wings. Once the rotorcraft is at a sufficient forward velocity, the required lift generation is transferred from the rotor to a canard and horizontal tail. Flap deployment would off load the spinning center wing, which could then stop rotation and be locked into a position across the fuselage to perform as a third wing. The flaps on the other two wings would then be retraced and all three wings would share the lift loads in a fixed wing flight mode. A reverse of these events would transition the CRW back to its rotary wing--VTOL mode for landing on small landing areas.

By using a reaction-drive rotor system, the CRW concept eliminates the need for a mechanical drive train and transmission, as well as the need for an anti-torque system. Eliminating these typically heavy, maintenance-intensive systems will greatly reduce vehicle weight, maintenance, complexity, and cost. Because the CRW's rotor is stopped to allow high-speed forward flight, the rotor's airfoil cross section must be elliptical. This is a compromise between the optimum airfoil shape for conventional rotor flight and that for high-speed stopped-rotor flight.

Possible manned and unmanned missions for such a vehicle include reconnaissance, communications and data relay, logistics re-supply, urban operations and delivery of both lethal and non-lethal munitions. The Navy and Marine Corps have expressed a strong interest in the CRW concept for both tactical UAV applications requiring VTOL operations from small-deck ships and manned applications such as a V-22 Osprey escort. They have funded a portion of the research activities to date and are considering transitioning this technology into a UAV engineering, manufacturing, and development phase following its successful flight demonstration.

In June 1998 a $24 million agreement between the Defense Advanced Research Projects Agency (DARPA) and The Boeing Company funded a 37 month effort by the Boeing Phantom Works to design, build and fly two technology demonstrators to assess and validate this advanced rotorcraft. DARPA and Boeing agreed to a 50/50 cost share agreement to validate this revolutionary concept in a joint advanced technology demonstration program known as "Dragonfly". Each contributed $12 million toward the program, initially planned to lead to flight demonstration in early 2001.

Development of the technology demonstrators is being conducted by Phantom Works personnel in Mesa, Ariz., St. Louis, Mo., as well as several other Boeing facilities. Final assembly is now under way at the Mesa facility, with a first flight expected in 2002.

On 04 December 2003 the Boeing Company's Canard Rotor/Wing (CRW) concept demonstrator completed its first hover flight at the U.S. Army Proving Ground in Yuma, Ariz. During the flight test, the CRW advanced technology demonstrator – known as the X-50A Dragonfly – flew for about 80 seconds at 8:10 a.m. MST. It lifted off vertically from the launch site to an altitude of 12 feet above the ground, hovered and then vertically landed, commencing the flight test program.

The unmanned X-50A CRW has a length of 17.7 feet and is 6.5 feet high. The rotor blades have a diameter of 12 feet. Powered by a conventional turbofan engine, the X- 50A will utilize diverter valves to direct thrust to the rotor blade tips (for helicopter mode), or aft to the jet nozzle (for fixed wing mode). Dual bleed thrust will be used during transition. By directing thrust through the rotor tips, the CRW concept eliminates the need for a heavy and complex mechanical drive train, transmission and anti-torque system. The CRW will be much lighter and simpler than traditional rotorcraft and will therefore be much cheaper to operate and support.

Follow-on CRW versions could evolve into larger, piloted vehicles capable of conducting specialized missions, including reconnaissance, armed escort, urban operations, tactical air support, communications/data relay and resupply. With such flexibility, operations could originate from small-deck ships or forward bases.

Aviation enthusiasts may have noticed that the X-50 designation was not the next in line. But Boeing's X-50 program manager Steve Bass said that Boeing got the number out of sequence by special request because the X-50 designation is so fitting for the CRW concept - 50 percent helicopter and 50 percent airplane.

## RQ-16 T-Hawk

http://en.wikipedia.org/wiki/RQ-16_T-Hawk

video:  http://www.honeywell.com/sites/portal?smap=aerospace&page=mav_video&theme=T8

## Vigilante

http://fas.org/irp/program/collect/vigilante.htm

## Baldwin MonoTiltRotor

http://www.baldwintechnology.com/

http://en.wikipedia.org/wiki/Mono_tiltrotor